## Slide 1
GasSentinel
Detecting Gas Leaks with IoT
Domenico Lattari
Shlok Bharuka

## Slide 2
  Safety concern
  Accident prevention
  Prompt alerts can save lives and properties
  Each device will be registered to an email and a certain address/location.
Application context

## Slide 3
  Detection Accuracy: must detect gas concentrations accurately and reliably.
  Real-Time Alerts: immediate alerting through buzzer and LED.
  Data Communication: transmit data to a central server and nearby devices.
  Compliance: must meet European safety standards for gas leaks detection.
Requirements

## Slide 4
ESP32S3 + antenna
MQ2 gas sensor
LEDs
Buzzer
Components

## Slide 5
LEDs
  GREEN: the system is on and working.
  YELLOW: peer gas leak.
  RED: gas leak detected.

## Slide 6
Technologies
  ESP-NOW: edge devices communication.
  MQTT: from edge to server communication (TLS).
  Python : server to store and analyse data.

## Slide 7
  Edge : monitoring, data collection (alert duration, sensor value), P2P communication , server communication.
  Cloud : data storage, geographical trends of leakages, remote alert (email).

## Slide 8
Challanges
  Sensor calibration: meet the european costraints.
  ESP-NOW: walls might be a problem.
  Placement of the device: distance from gas source and peer.
  Energy consumption: battery feasibility.

## Slide 9
Sensor calibration
  Voltage output: the sensor outputs a value between 0 to 5v
  PPM : retrieve the part per milion of the gas
  LEL : lower explosion limit of LPG is 20,000 ppm
  Trigger : 10% of LEL (key requirements from EN 50194-1 and EN 50194-2)

## Slide 10
ESP-NOW
  Wi-Fi channel : using both Wi-Fi and ESP-NOW might lead to unreliable P2P communication.
  Antenna : might not be enough to communicate through walls.

## Slide 11
Device placement
  Position of the sensor : distance from the source (e.g. gas stove, boiler, gas storage)
  Position in respect to peer devices